## Slide 1: Saeedah Asaf, MD, MBBS Arkansas Children’s Hospital, Little Rock, AR, USA The Children’s Hospital, Lahore, Pakistan Andrew Infosino, MD Health Sciences Clinical Professor Benioff Children’s Hospital San Francisco
Vascular Access in Infants and Children

## Slide 2: Disclosures
No relevant financial relationships

## Slide 3: Learning Objectives:
Indications and techniques of PIV insertion
Central venous access: Indications, sites, complications and technique
Arterial line: indications, sites and technique
Ultrasound for vascular access
Intraosseous lines: Indications, sites, technique & complications

## Slide 4: Peripheral IV Access

## Slide 5: Peripheral IV Access
Indication: Administration of medicines, fluids
Common sites are: Saphenous, foot, Back of hand, base of thumb, antecubital, Cephalic or Basilic vein
Complications: Extravasation, thrombosis, infection
Minimize complications:
  Frequent assessment of site, limb elevation,
  Avoid dessicants through PIV: Dextrose 10% or higher, KCl or Calcium, Bicarbonate

## Slide 6: Difficult PIV
Reassess need for PIV
Consider Midline catheter (MLC) or Peripherally inserted central catheter (PICC) if anticipated stay > 5 days
Consider ultrasound guided PIV
https://youtu.be/d8VFgb9Edfw

## Slide 7: Out of Plane Technique For Ultrasound Guided PIV
Preliminary scan to choose the best site
Basilic vein is a large and superficial vein on the medial side of the arm.
Highest success: vessel depth 0.3 - 1.5 cm and diameter 0.4 cm or greater
Deeper veins require longer angiocath
Clean the area with alcohol or chlorhexidine
Apply tourniquet

## Slide 8: Out of Plane Technique For Ultrasound Guided PIV (con’t)
High frequency linear probe: adjust depth (2 cm or less
Bring the target in the middle of the screen
Start needle insertion 0.5 to 1 cm away from the probe at 45 degree angle aiming for “bulls eye” in the vein
Tilt the probe towards the needle to confirm and then follow needle tip position as it enters the vein
Drop the angle and advance catheter in the vein keeping it in the center
Thread the catheter off the needle and confirm placement.
Secure catheter in place.

## Slide 9: Central Venous Access

## Slide 10: Central Venous Access
Indications: vasopressors, dessicants, hyperalimentation, inadequate PIV, or anticipated major fluid shift
Review medication, check coags, platelets and correct if indicated
Contraindications: No absolute contraindication, but consider sites that minimize complications if pre-existing coagulopathy or thrombocytopenia
Complications: Central line associated blood stream infection (CLABSI), hematoma, thrombosis, pneumothorax, hemothorax
CLABSI is preventable!
https://youtu.be/R0ee3apcgS4

## Slide 11: Central Venous Access
Site Selection:
Internal jugular vein (IJV): easiest to cannulate
Subclavian vein: higher risk of pneumothorax or hemothorax
Femoral vein may be preferable in coagulopathic patients as it can be compressed easily
Brachiocephalic vein although an advanced technique, is particularly helpful in collapsed or edematous infants and neonates
Axillary vein

## Slide 12: Know Your Anatomy https://youtu.be/xuuxPUQoWgE https://youtu.be/UJrOl4GFtmI

## Slide 13: CVL: Size and Insertion Depth
Weight (kg) | Internal Jugular or Subclavian Catheter size | Internal Jugular or Subclavian Insertion Depth (cm) | Femoral Vein Catheter Size | Femoral Vein Insertion Depth (cm)
< 10 Kg | 4 Fr, 2 lumen | 8 | 4Fr, 2 lumen | 12cm
12 - 30 kg | 4 Fr, 2 lumen | 12 | 4Fr, 2 lumen | 12 - 15
30 - 50 kg | 5 Fr, 2 lumen | 12 - 15 | 5 Fr, 2 lumen | 15
50 - 70 kg | 7 Fr, 2 lumen | 15 | 7 Fr, 2 lumen | 20
> 70 kg | 8Fr, 2 lumen | 16 | 8 Fr, 2 lumen | 20
Reference: Anesthesia for Congenital Heart disease. Dean Andropoulus, Second Edition.2010

## Slide 14: Central Venous Access Techniques
Ultrasound Guided vs Palpation:
Ultrasound use for vascular access has become the standard of care for the placement of central lines
Decreased incidence of complications including pneumothorax and accidental arterial puncture
Helpful in collapsed or edematous infants and neonates
Utilize palpation technique if no ultrasound is available, but must be familiar with anatomy

## Slide 15: Internal Jugular Vein: Palpation Technique
Right side: Avoid left if possible to avoid injury to thoracic duct
Position: shoulder roll to extend neck, head turned away 30 to 45 degrees, Trendelenburg position
Proper sterile technique: pre-procedure hand washing, hat, face mask, sterile gown and gloves and skin prep and drape
Central line kit: flush and clamp all ports with saline except for distal port
Central line kit should be placed in an ergonomic position (e.g. right handed individual should place kit on the right side of the patient)

## Slide 16: Internal Jugular Vein: Palpation Technique (con’t)
Palpate the carotid artery at the level of the cricoid cartilage
Insert needle or angiocath just lateral to the carotid pulse at 45 degree angle towards the ipsilateral nipple and confirm free flow of non-pulsatile blood
Pass J tip wire through needle or angiocath while monitoring ECG for PVCs and then remove needle or angiocath
Make a small skin nick with a scalpel at wire insertion site
Carefully place dilator, then remove, then place central venous catheter over wire using Seldinger technique and secure by suturing and place sterile dressing
https://youtu.be/GfFdr3DFjlA

## Slide 17: Subclavian Vein: Palpation Technique
Position: shoulder roll, Trendelenburg position, turn head 10 - 20 degrees towards the same side to compress the internal jugular vein
Proper sterile technique: pre-procedure hand washing, hat, face mask, sterile gown and gloves and skin prep and drape
Central line kit: flush and clamp all ports with saline except for distal port
Central line kit should be placed in an ergonomic position (e.g. right handed individual should place kit on their right side)

## Slide 18: Subclavian Vein: Palpation Technique (con’t)
After sterile prep and drape, insert needle of angiocath just lateral to the mid-clavicular point towards the suprasternal notch just underneath the clavicle
Confirm free flow of non-pulsatile blood
Pass J tip wire through needle or angiocath while monitoring ECG for PVCs and then remove needle or angiocath
Make a small skin nick with a scalpel at wire insertion site
Carefully place dilator, then remove, then place central venous catheter over wire using Seldinger technique and secure by suturing and place sterile dressing
Pulling the ipsilateral arm caudad may open the space between the rib and clavicle making insertion easier

## Slide 19: Femoral Vein: Palpation Technique
Position: place a small roll under the hips with both thighs slightly abducted
Proper sterile technique: pre-procedure hand washing, hat, face mask, sterile gown and gloves and skin prep and drape
Central line kit: flush and clamp all ports with saline except for distal port
Central line kit should be placed in an ergonomic position (e.g. right handed individual should place kit on their right side)

## Slide 20: Femoral Vein: Palpation Technique (con’t)
Palpate the femoral artery just below the inguinal ligament which runs from anterior superior iliac spine and the pubic symphysis
Insert needle or angiocath just medial to the femoral artery pulse towards the umbilicus and confirm free flow of non-pulsatile blood
Pass J tip wire through needle or angiocath while monitoring ECG for PVCs and then remove needle or angiocath
Make a small skin nick with a scalpel at wire insertion site
Carefully place dilator, then remove, then place central venous catheter over wire using Seldinger technique and secure by suturing and place sterile dressing

## Slide 21: Post Central Line Placement
Obtain chest X-ray immediately after internal jugular or subclavian central line placement
Confirm correct placement with tip of catheter in SVC or at SVC - RA junction
Rule out pneumothorax
Obtain KUB after femoral line placement to confirm correct placement

## Slide 22: Ultrasound Guided Vascular Access

## Slide 23
Key to Success: Needle tip must be continuously visualized and only advanced under ultrasound guidance
Ultrasound Guided Vascular Access

## Slide 24
Ergonomics: position the ultrasound machine in front of the proceduralist
Choose the appropriate transducer based on patient size and depth of target
Adjust depth so that the target vessel is in the middle of the screen
Align the transducer so that the left side of the screen is the left side of the transducer
Adjust gain so that the target can be distinguished from the surroundings
Superficial vascular structures are best seen with high frequency linear probe (8 to 16mhz)
Ultrasound Guided Vascular Access

## Slide 25
Four key transducer manipulations: Sliding, rotating, tilting and rocking
Pre-scan both sides and choose the side with the best anatomy
Arteries and veins appear as anechoic or black; needles, bones and pleura appear bright or hyper-echoic
  Arteries: thick walled, round black structures, not easy to collapse with pressure
  Veins: thin walled, oval structures that collapse with pressure
Color doppler with pulsatile flow in the artery can help distinguish arteries from veins
A midline guide is helpful in placing the transducer mid marker immediately over the target vessel
Ultrasound Pearls:

## Slide 26: Ultrasound Transducer Manipulation
https://youtu.be/RskrEsAGzec
https://youtu.be/QAJ5rbJua7U

## Slide 27
Usual Anatomic Relationship and Variations
Internal jugular vein is usually anterolateral to the carotid artery, but may be anterior, or lateral or posterolateral to the artery
Femoral vein is usually posteromedial to the femoral artery, but may be anteromedial, posterior and even lateral
Subclavian vein is usually anterior to the subclavian artery

## Slide 28: Ultrasound Guided Internal Jugular Vein Access
Place a small shoulder roll and turn the head about 30 degrees to the opposite side.
After prep and drape, cover the probe with a sterile sheath.
Hold the transducer in non-dominant hand between thumb and forefingers, and rest hand on patient to stabilize and support the transducer
Scan the trachea to identify the cricoid ring

## Slide 29: Ultrasound Guided Internal Jugular Vein Access (con’t)
Scan laterally from cricoid ring to identify the carotid artery (round, pulsatile)
Then identify the internal jugular vein lateral to the carotid artery (thin walled, collapsible, non-pulsatile)
Scan the internal jugular vein vein to ensure patency and no thrombus
Center the internal jugular vein on the ultrasound screen
Insert needle at 45 degrees about 0.5 - 1 cm away from the transducer

## Slide 30: Ultrasound Guided Internal Jugular Vein Access (con’t)
Dynamic Needle Tip Tracking (DNTT)
Align center of the vein with the center line of the transducer
Tilt the transducer towards the needle to locate the needle tip (white hyperechoic dot) and follow the needle as it is advanced to the center of the vein
DNTT is crucial for success minimizing complications and requires small movements of the needle and transducer

## Slide 31: Ultrasound Guided Internal Jugular Vein Access: Pearls
Valsalva maneuver or pressure on the liver can help distend the internal jugular
Visualize the wire with ultrasound and confirm that it is in the vein prior to dilation
Confirm placement of the catheter with ultrasound

## Slide 32: Ultrasound Guided Supraclavicular Approach to Brachiocephalic Vein
The subclavian vein joins the IJV to form the brachiocephalic vein or innominate vein.
In plane approach with high frequency hockey stick, linear transducer
Operator stands on the same side with ultrasound on the opposite side
Risk of pneumothorax is minimized by keeping the entire needle under vision as it is advanced towards the vein

## Slide 33: Supraclavicular Approach to Brachiocephalic Vein
Anatomical view of the cervicothoracic region. (A) Frontal view outlining the different angles of puncture between right and left sub­clavian (SCV) and brachiocephalic (BCV) veins. CA, carotid artery; IJV, internal jugular vein; EJV, external jugular vein. (B) Left SCV approach: the probe is slid (1) down perpendicular to the IJV and tilted anteriorly (2) toward the L­SCV. Noted that the left subclavian artery (L­SCA) is running posteriorly to the aorta. (C) Right SCV approach: Similarly, to the left side approach, the probe is slid down the IJV (1), than tilted anteriorly (2). Noted the close relation of the right ­SCV and right­ SCA
Frontiers of Pediatrics. Zied Merchaoui 05 October 2017 doi:10.3389/fped.2017.00211

## Slide 34: Ultrasound Guided Supraclavicular Approach to Brachiocephalic Vein: Technique
Place ultrasound transducer horizontally at the level of the cricoid ring and find the carotid artery
Then identify the internal jugular vein lateral to the carotid artery and follow it down to the supraclavicular region
Keep the internal jugular vein in the center of the screen and turn the transducer in the antero-posterior plane to look into the thoracic inlet to visualize the brachiocephalic vein

## Slide 35: Ultrasound Guided Supraclavicular Approach to Brachiocephalic Vein: Technique (con’t)
Utilize the in plane approach and advance the needle into the brachiocephalic vein at about a 20 to 30 degree angle taking care to avoid the hyperechoic first rib and the lung
Once free flow of blood is noted use the Seldinger technique to advance the wire, remove the needle, insert the dilator and then the central line
Secure central line with suture and then place a sterile dressing
Confirm placement with chest X-ray

## Slide 36: Ultrasound-Guided Supraclavicular Subclavian Vein Catheterization in Children
https://youtu.be/FrgSkmpuHmI

## Slide 37: Femoral Vein Access
Femoral vein catheters are associated with a higher incidence of thrombosis than internal jugular catheters
May be useful in head and neck procedures
Safer in patients with coagulopathies or thrombocytopenia as direct pressure can be applied
Preferred site in single ventricle patients

## Slide 38: Femoral Vein Access: Ultrasound Technique
Position patient with hip externally rotated
Sterile prep and drape
Place the prove transversely just below the inguinal ligament
Identify the femoral artery (pulsatile flow)
Identify the femoral vein medial to the femoral artery

## Slide 39: Femoral Vein Access: Ultrasound Technique (con’t)
Bring the vein to the middle of the ultrasound screen and align with the middle of the transducer
Insert needle approximately 1 cm caudad to transducer at a 30 - 45 degree angle
Utilize Dynamic Needle Tip Tracking to place needle in the center of the femoral vein
Use Seldinger technique to place the femoral venous catheter

## Slide 40: ARTERIAL ACCESS

## Slide 41: Arterial Access
Indications: provides continuous pressure monitoring in cases with hemodynamic instability, large fluid shift or blood loss, cardiopulmonary bypass, deliberate hypotension or need for frequent arterial blood monitoring
Complications: infection, hematoma, distal ischemia, proximal emboli, thrombosis and arterio-venous fistula

## Slide 42: Arterial Catheter Sizing Recommendations
Neonates (< 5 kg): 24 GA angiocath
Infants (5-10 kg): 24 or 22 gauge angiocath
Toddlers (10-20 kg): 22 gauge angiocath
Children (20-50 kg): 22 or 20 gauge angiocath
Teenagers (>50 kg): 20 gauge angiocath

## Slide 43: Arterial Catheter Site Recommendations
Ideal Site:
  Collateral blood flow
  Not affected by surgery or vascular clamps
Radial Artery: preferred site as easily palpable and usually good collateral blood flow
Femoral artery: largest superficial vessel and often used during severe hypotension, arrest or trauma

## Slide 44: Arterial Catheter Site Recommendations (con’t)
Less optimal sites:
Brachial artery: poor collateral flow and potential for median nerve injury
Ulnar artery at wrist: avoid if radial artery has decreased flow
Dorsalis pedis and posterior tibial arteries: pressure waveform may be amplified up to 30% compared with aortic pressures
Superficial temporal artery: associated with stroke

## Slide 45: "Arterial Line Placement" by James DiNardo, MD, FAAP for OPENPediatrics
https://youtu.be/3z9vHu4r6HE

## Slide 46: Radial Artery: Catheter Over Needle Technique (Angiocath)
Extend wrist and stabilize by taping to wrist splint or IV board
Wash hands and use sterile gloves
Sterile prep and drape
Palpate the radial artery with non-dominant hand at the level of the wrist
Insert angiocath at approximately 20 to 30 degree angle
When there is evidence of blood return, decrease the angle of the angiocath and advance it 1-2 mm and then slide the catheter into the artery and remove the needle
Confirm waveform with transducer and apply sterile dressing

## Slide 47: Radial Artery: Seldinger Technique
Similar preparation and positioning as Angiocath technique
Insert angiocath at 45 degree angle through the radial artery and then remove the needle and slowly withdraw the catheter until there is pulsatile blood flow
Insert a soft tip guide wire through the angiocath
Advance the catheter over the wire and then remove the wire.
Attempt should be abandoned if there is any resistance to wire and start over again.
This technique can also be used to upsize arterial catheters either from a 24 to a 22 gauge angiocath or a 22 to a 20 gauge angiocath

## Slide 48: Femoral Artery Cannulation
Mild external rotation of the lower extremity at the hip
Wash hands and use sterile gloves
Sterile prep and drape
Palpate the femoral artery with non-dominant hand just below the inguinal ligament
Utilize a 22 gauge angiocath in infants and a 20 gauge angiocath in children and teenagers
Insert angiocath at approximately 20 to 30 degree angle
When there is evidence of blood return, decrease the angle of the angiocath and advance it 2-3 mm and then slide the catheter into the artery and remove the needle
Confirm waveform with transducer and apply sterile dressing

## Slide 49: Ultrasound Guided Arterial Access
Both short axis and long axis techniques can be utilized
Can identify anatomic variations and thrombosis
Sterile prep/drape and probe cover

## Slide 50: Intraosseous Access

## Slide 51: Intraosseous Access
Intraosseous (IO) access can be used to deliver fluids and medications directly into the bone marrow when intravenous access cannot be established quickly (e.g. trauma or severe dehydration)
Recommendation: Remove IO needle within 24 hours to to minimize potential for osteomyelitis once intravenous access has been established

## Slide 52: Intraosseous Access
IO sites:
  proximal tibia, distal tibia, distal femur, iliac crest, proximal humerus and sternum
  Preferred site in children is the anteromedial aspect of proximal tibia
Contraindication: Infection or burn at the site, fracture proximal to the chosen site, osteoporosis, osteopenia or osteogenesis imperfecta.
Complications: Extravasation, osteomyelitis and fracture.

## Slide 53: Intraosseous Access: Technique
Prep skin with chlorhexidine
Advance interosseous needle through the cortex till (loss of resistance and ability to aspirate blood/bone marrow)
Secure needle and ensure that intravenous fluid flows freely without extravasation
If intraosseous needles are not available, any hollow borrow needle can be used such as an 18 or 20 gauge spinal needle
Various intraosseous systems (e.g. EZ-IO) offer weight based needle sizes and drill assisted insertion

## Slide 54: Instructional Videos
Ultrasound guided subclavian central lines
https://youtu.be/_VYHj4sRlkc
Central line insertion, kit and equipment focus
https://youtu.be/nQwExKXMy6w
Central venous line sterile prep
https://youtu.be/5ZGHBjVQD9Y
Lateral approach to IJV/ BCV
https://www.csurgeries.com/video/vascular-video/

## Slide 55: Conclusions:
Intravenous access should be established in a safe and timely manner
Anesthesia providers should choose the route and site based on the patient’s condition, available resources and familiarity with the technique
Ultrasound use decreases complications and enhances safety

## Slide 56: References:
Jöhr M, Berger TM. Venous access in children. Current Opinion in Anesthesiology. 2015;28(3):314–320.
Ares G, Hunter CJ. Central venous access in children. Current Opinion in Pediatrics. 2017;29(3):340–346.
Saugel B, Scheeren TWL, Teboul JL. Ultrasound-guided central venous catheter placement: a structured review and recommendations for clinical practice. Crit Care. 2017;21(1):225.
Paladini A, Chiaretti A, Sellasie KW, Pittiruti M, Vento G. Ultrasound-guided placement of long peripheral cannulas in children over the age of 10 years admitted to the emergency department: a pilot study. BMJ Paediatr Open. 2018;2(1):e000244.
Takeshita J, Yoshida T, Nakajima Y, et al.Superiority of Dynamic Needle Tip Positioning for Ultrasound-Guided Peripheral Venous Catheterization in Patients Younger Than 2 Years Old. Pediatric Critical Care Medicine. 2019;20(9):e410–e414.
Liu L, Tan Y, Li S, Tian J. “Modified Dynamic Needle Tip Positioning” Short-Axis, Out-of-Plane, Ultrasound-Guided Radial Artery Cannulation in Neonates. Anesthesia & Analgesia. 2019;129(1):178–183.
Banerjee S, Singhi SC, Singh S, Singh M. The intraosseous route is a suitable alternative to intravenous route for fluid resuscitation in severely dehydrated children. Indian Pediatr. 1994 31(12):1511-20.
Anesthesia for Congenital Heart Disease. Dean B. Andropoulos, M.D., M.H.C.M. Second Edition.2010.
Smith’s Anesthesia for Infants and Children. Peter J. Davis, Franklyn P. Cladis. Ninth Edition. 2016.
Point-of-Care Ultrasound. Nilam J.Soni. Second Edition.2019.
Misplaced central venous catheters: applied anatomy and practical management. Gibson , F. et al.British Journal of Anaesthesia, 2013;Volume 110, Issue 3, 333 – 346.
Merchaoui Z, Lausten-Thomsen U, Pierre F, Ben Laiba M, Le Saché N, Tissieres P. Supraclavicular Approach to Ultrasound-Guided Brachiocephalic Vein Cannulation in Children and Neonates. Front Pediatr. 2017;5:211.
Hanada, S. , Van Winkle, M. T., Subramani, S. and Ueda, K. (2017), Dynamic ultrasound‐guided short‐axis needle tip navigation technique vs. landmark technique for difficult saphenous vein access in children: a randomised study. Anaesthesia, 2017;72: 1508-1515.
Ultrasonographic anatomic variations of the major veins in paediatric patients. Neto, E. P. Souza et al..British Journal of Anaesthesia, 2014;Volume 112, Issue 5, 879 - 884.
Vezzani A, Manca T, Vercelli A, Braghieri A, Magnacavallo A. Ultrasonography as a guide during vascular access procedures and in the diagnosis of complications. J Ultrasound. 2013;16(4):161-170.